Thesis Defense
KAU/RH PhD supervision
Breakdown of the Eiffel paper
by Frey Alfredsson
- cFFS
- Gradient Queue
- PIFO changes

---
Eiffel overview
- Main objective: The design and implementation of efficient and flexible packet scheduling in software
- Difficulties:
  - Simple scheduling policies are CPU intensive
  - Comparison-based priority queues rely on O(log n)
    - Or O(m log n) with m priority queues
- Contributions
  - An optimization for ExtractMin and ExtractMax
  - A method to make binary structures circular
  - Modified PIFO for better flexibility in software

---
Eiffel flow: Packet flow

---
Find First Set (FFS)
- A bitmap represents the occupied queues
- Most CPUs have FFS instructions that can find the min and max set bits

---
Eiffel flow
Queues that have more than CPU word size queues can be split into a binary tree

---
FFS in code
for (w = 0; w < bq_count; w++) {
  while ((i = ffs(bq[w])) {
    /* work on bq_data[w][i] */
  }
}

---
Circular Find First Set
- cFFS uses a buffer for lower priority flows
  - After the primary scheduling queue is processed the primary queue is swapped with the Secondary queue
- Flows with a higher priority than available are stacked in the last queue

---
Gradient Queue / (Approximate Gradient Queue)
- The set binary values are combined into a value x
- A weight function is calculated using each value at position i
  - Weight function 2^(i)(x-i)^2
- Using the the equation ax^2-bx+c and that there is only one solution (x = b/2a), the position is ceil(b/a)

---
Eiffel PIFO changes
- Eiffel PIPO changes
  - Per flow ranking and scheduling
  - Can schedule on dequeue

---
Traffic shaping policy

---
Traffic shaping queue view